## Slide 1
Five Missions, Quantified
Mission UQ v1.1: how each mission's uncertainty is calculated, which drones fit, the weather on the fires, and where drones fit hour by hour
NASA Aerial Wildfire Project | ACERO Disaster Lab working group | 20 October 2026 | Standard day: 24 h, 06:00 to 06:00, peak-run day | GOFER not used
Notes: Title. This deck has two slides per mission document, M1 to M5, version 1.1. Every number comes from data in the project folder: station weather (Weather Data), the perimeter time-area records (perimeter_supplements, GOFER rows removed), the Week 6 workbook and the v0.5 proposal. Each mission is evaluated on the same standard day: 24 hours, 06:00 to 06:00 local, on that fire's peak-run day (Camp 8 to 9 Nov 2018, Carr 26 to 27 Jul 2018, Pioneer 29 to 30 Aug 2016, LNU 18 to 19 Aug 2020).

## Slide 2
M1 | FIRELINE MAPPING | BOTTOM LINE
The map is the uncertainty: how old it is, and whether drones can keep it fresh
NASA Aerial Wildfire Project | ACERO Disaster Lab | Mission UQ v1.1 | 20 October 2026
2
18 h
Oldest the newest aircraft perimeter got during Carr's 26 July run; every listed drone could fly all 24 hours
4% of hours
Camp standard day: hours an Alta X could fly by gusts at Jarbo Gap, so its map would be most of the day old
1.7 h
Expected map age at Camp for a Type 1 rated to 30 mph on a 1 h revisit (about 7,700 ac unmapped)
Who uses it
Incident commander and planning: map age decides whether resource orders and evacuation triggers rest on a current line.
Division supervisors and lookouts: head and flank position, refreshed within the hour.
Drone types and parameters
FVR-90, Type 1 FW: 12 to 18 h, thermal video, wind limit not found
SuperVolo: 8 h, relay and second mapping tier
Alta X, Type 3: 17 min sorties, 22 mph
SwitchBlade-Elite: 18 min sorties, 25 mph
Notes: M1 fireline mapping, bottom line. The quantity is information age: how old the newest fireline map is when someone uses it. First card: on Carr the newest aircraft perimeter reached 18 hours old during the run, while station wind would have let every listed drone fly every hour. Second card: on Camp an Alta X read against gusts could fly in only 4% of hours, so its map would be most of a day old. Third card: a Type 1 fixed wing rated to 30 mph flies 46% of Camp hours and keeps the expected map age near 1.7 hours. The formula is on the next slide's notes. p, the wind gate, is the share of hours in the standard day when the station wind is at or under the drone's wind limit. Read on sustained wind (10-minute mean) it is the optimistic value; read on gusts (peak in the hour) it is the conservative value. Both are measured 20 ft above ground, so wind at flight altitude is stronger and both overstate availability.

## Slide 3
M1 | FIRELINE MAPPING | HOUR BY HOUR
Carr, 26 to 27 July: the line moved while the record stood still
NASA Aerial Wildfire Project | ACERO Disaster Lab | Mission UQ v1.1 | 20 October 2026
3
Hour
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
23
00
01
02
03
04
05
Gust mph
19
20
20
17
18
14
12
10
9
9
11
9
21
14
13
12
20
20
18
14
13
14
14
14
Alta X 22
Type 1 at 30
Map age h
11
12
13
14
15
16
17
18
1
2
3
0
1
2
3
4
5
6
1
2
3
4
5
6
Drone task
Fresh perimeter for the morning plan; decide where the line and resources go
Type 1 holds whole-fire perimeter; Type 3 maps the active east flank
Track the run hourly: head, spots across the river; push the line to IC and divisions
Night IR perimeter by Type 1 so the morning plan starts from a current line
Night IR passes on spots and flanks; fresh perimeter before the briefing
Green: can fly by station gusts. Red: grounded. Dark hour cells: night (20:00 to 06:00). Map age: hours since the newest aircraft perimeter in the record.
What the records show
17:30 Run east at 2.5 mph, spotting over 1 mile; 17:34 aircraft perimeter 44,484 ac
19:17 Spots east of the Sacramento River; 19:20 to 20:00 vortex on radar
19:45 ICS-209 28,763 ac, unchanged at 20:15 and 21:00
00:00 Next aircraft perimeter 50,050 ac; spots south of Whiskeytown Lake
Night 10% of Carr aircraft perimeters were flown at night, but about 28% of growth fell at night
Quantified uncertainty
E[A] = R (2 - p) / (2p). Carr: p = 100%, so a 1 h revisit holds the map near 0.5 h old. Camp: 0.9 h if the limit is read on sustained wind, 23.3 h on gusts.
Largest unknowns: sustained versus gust reading, and the unpublished Type 1 wind limit.
Notes: M1 calculation. Expected map age E[A] = R (2 - p) / (2p). R is the revisit interval: the time between scheduled mapping passes, 1 hour here. p is the chance a scheduled pass actually flies, the wind gate. E[A] is the expected age of the newest good map at a random moment. Why the formula: when each pass succeeds with probability p, the time between good maps is R times a geometric number of tries; averaging the age over that gap gives R (2 - p) / (2p). Check: if p = 1 every pass flies and E[A] = R/2, half the revisit interval. Camp: p = 1 on sustained wind gives 0.9 h; p = 4% on gusts gives 23.3 h, longer than the day itself, which means no useful map. Map error E(t) = G x A(t): G is the fire's growth rate in acres per hour (Camp: more than 55,000 acres in the first 12 hours, about 4,600 ac/h, from the CAL FIRE Green Sheet in the Camp record), and A(t) is the map age, so E is the area burned since the map was made. How to read the hour strip: one column per hour of the standard day (06:00 to 06:00 local on the peak-run day). Gust mph is the peak wind in that hour at the station named on the document (red when above 30 mph). Alta X 22 and Type 1 at 30 are fly or no-fly: green when that hour's gust is at or under the drone's wind limit, red when above. Map age h is hours since the newest aircraft perimeter in the record. The coloured bars are the drone task we propose for each phase.

## Slide 4
M2 | SPOT FIRE DETECTION | BOTTOM LINE
Spot fires: detection time depends on whether the drone can fly at all
NASA Aerial Wildfire Project | ACERO Disaster Lab | Mission UQ v1.1 | 20 October 2026
4
32 to 779 min
Expected time for an Alta X to find a spot at Camp, from the sustained to the gust reading (30 min search, Pd 0.9 assumed)
85 min
First 911 call to first burnovers at Camp: the clock every detection competes with
58 min
Same search by a Type 1 rated to 30 mph, read on gusts
Who uses it
Lookouts and division supervisors: a spot across the line changes escape routes and safety zones within minutes.
Incident commander: whether initial attack reaches a spot before it becomes a new front.
Drone types and parameters
Type 1 / 2 FW: 6 to 14 h mid-wave IR, 1 to 6 h long-wave IR
Alta X / SwitchBlade-Elite: initial attack size-up, confirm hot spots
Mavic 2 EA (sensor reference): 640 x 512 thermal, 8 to 14 µm, saturates at 550 °C
Notes: M2 spot fire detection, bottom line. The quantity is the expected time from a spot fire starting to a drone seeing it. First card: an Alta X searching every 30 minutes on Camp's standard day takes 32 minutes if its wind limit is read on sustained wind and 779 minutes on gusts, because it is grounded most hours. Second card: 85 minutes is the time from the first 911 call (06:25) to the first burnovers (07:50) at Camp, the clock any detection competes with; it is a comparison, not a deadline. Third card: a Type 1 rated to 30 mph doing the same search, read on gusts, takes 58 minutes. p, the wind gate, is the share of hours in the standard day when the station wind is at or under the drone's wind limit. Read on sustained wind (10-minute mean) it is the optimistic value; read on gusts (peak in the hour) it is the conservative value. Both are measured 20 ft above ground, so wind at flight altitude is stronger and both overstate availability.

## Slide 5
M2 | SPOT FIRE DETECTION | HOUR BY HOUR
Camp, 8 to 9 November: initial attack in wind that grounded small drones
NASA Aerial Wildfire Project | ACERO Disaster Lab | Mission UQ v1.1 | 20 October 2026
5
Hour
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
23
00
01
02
03
04
05
Gust mph
40
28
25
21
30
29
33
32
24
28
25
23
27
30
34
36
39
43
48
45
48
41
47
45
Alta X 22
Type 1 at 30
Map age h
none
none
none
0
1
2
3
4
5
6
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Drone task
Initial attack
Search ahead of the
Wide-area IR search downwind; confirm spots that threaten evacuation routes
Night IR search for spots outside the line; send positions to night operations
Night IR search; list confirmed spots for the morning briefing
Green: can fly by station gusts. Red: grounded. Dark hour cells: night (20:00 to 06:00). Map age: hours since the newest aircraft perimeter in the record.
What the records show
06:25 First 911 call; 06:44 first engine reports about 35 mph wind; 06:45 second ignition
07:10 Engine estimate 200 to 300 ac; 07:37 Concow order; 07:50 first burnovers
08:01 Air attack: 'fire is now in Paradise', about 2,000 ac
09:54 First aircraft perimeter: 54,586 ac
Night Camp night gusts grounded an Alta X in 38% of night hours
Quantified uncertainty
E[T] = R/2 + R (1 - q)/q, q = p x Pd. Read on gusts: Alta X 779 min, SwitchBlade-Elite 145 min, Type 1 at 30 mph 58 min, against 85.
Pd has no operational record yet; v1.1 runs 50%, 80% and 95%.
Notes: M2 calculation. Expected detection time E[T] = R/2 + R (1 - q) / q, with q = p x Pd. R is the search revisit interval, 30 minutes (assumed). p is the wind gate, the chance the pass flies. Pd is the chance the sensor sees the spot on a pass that flies; no drone has an operational record, so it runs at 50%, 80% and 95%, with 90% on the headline numbers. q is the chance a single pass both flies and detects. R/2 is the average wait for the first pass; R (1 - q) / q is the average extra wait for the failed passes before the first success. Smallest detectable spot: A_min = (k x GSD) squared, where GSD = 2 h tan(HFOV / 2) / N is the ground size of one pixel. h is height above ground, HFOV is the camera's horizontal field of view (40 degrees assumed), N is pixels across (640 for the Mavic 2 EA thermal), and k is how many pixels across a spot must cover to be confirmed (3 assumed). At 60 m that is a pixel of about 7 cm; at 3,500 ft, the Type 1 floor, about 1.2 m. How to read the hour strip: one column per hour of the standard day (06:00 to 06:00 local on the peak-run day). Gust mph is the peak wind in that hour at the station named on the document (red when above 30 mph). Alta X 22 and Type 1 at 30 are fly or no-fly: green when that hour's gust is at or under the drone's wind limit, red when above. Map age h is hours since the newest aircraft perimeter in the record. The coloured bars are the drone task we propose for each phase.

## Slide 6
M3 | FIREFIGHTER SAFETY | BOTTOM LINE
Crew safety: the chance the fire wins, P(M < 0)
NASA Aerial Wildfire Project | ACERO Disaster Lab | Mission UQ v1.1 | 20 October 2026
6
10%
P(M < 0) at Camp's first burnovers, 45 min escape, Alta X overwatch, limit read on sustained wind
91%
Same case with the limit read on gusts: the drone is grounded most of the morning
21%
Carr 26 July, every drone flyable: risk left from a missed pass, relay retries and egress
Who uses it
Crews, lookouts, crew bosses: a warning must arrive with more time than the escape takes.
Division supervisors, safety officer: trigger points, escape routes, safety zones.
Incident commander: commit or pull a crew.
Drone types and parameters
FVR-90: overwatch and airborne relay (TCL 1)
SuperVolo: relay behind terrain
Alta X: escape routes, safety zones, landing zones
Matrice 200 v2: local wind profiles for trigger points
Notes: M3 firefighter safety, bottom line. The quantity is P(M < 0), the probability the fire reaches a crew before the crew has finished escaping. First card: Camp's first burnovers, 45-minute escape, Alta X overwatch with its limit read on sustained wind: 10%. Second card: the same case read on gusts: 91%, because the drone cannot fly most of that day. Third card: Carr on 26 July, where every listed drone could fly: 21%; the remaining risk comes from a missed detection pass, warning relay retries and the escape itself. p, the wind gate, is the share of hours in the standard day when the station wind is at or under the drone's wind limit. Read on sustained wind (10-minute mean) it is the optimistic value; read on gusts (peak in the hour) it is the conservative value. Both are measured 20 ft above ground, so wind at flight altitude is stronger and both overstate availability.

## Slide 7
M3 | FIREFIGHTER SAFETY | HOUR BY HOUR
Camp, 8 November: every crew hazard came before the record
NASA Aerial Wildfire Project | ACERO Disaster Lab | Mission UQ v1.1 | 20 October 2026
7
Hour
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
23
00
01
02
03
04
05
Gust mph
40
28
25
21
30
29
33
32
24
28
25
23
27
30
34
36
39
43
48
45
48
41
47
45
Alta X 22
Type 1 at 30
Map age h
none
none
none
0
1
2
3
4
5
6
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Drone task
Watch crews and engines
Overwatch of crews in Paradise; mark safety zones and blocked routes; relay warnings
Before and during firing
Reassess safety zones and helicopter landing zones for the night
Night overwatch of crews on the line; thermal view replaces the lookout
Night overwatch; confirm escape routes are open for the morning shift
Green: can fly by station gusts. Red: grounded. Dark hour cells: night (20:00 to 06:00). Map age: hours since the newest aircraft perimeter in the record.
What the records show
07:50 First burnovers on Hoffman and Concow roads, 85 min after the first call
14:15 Firing operation on Rattlesnake Flats Rd; 14:45 wind shift to about 25 mph
15:00 Emergency traffic call unanswered (radio volume); 15:15 burnover
18:30 First ICS-209: 16,000 ac
Quantified uncertainty
M = T_fire - (T_detect + T_notify + T_egress). P(M < 0) by escape time 30 / 45 / 60 min, Camp Alta X on gusts: 88% / 91% / 95%; Type 1 at 30 mph: 17% / 28% / 49%.
Escape time is the missing measurement: crew positions and routes are not in the records.
Notes: M3 calculation. Safety margin M = T_fire - (T_detect + T_notify + T_egress). The crew is safe when M is positive. T_fire is the time from the hazard becoming visible to fire reaching the crew: 85 minutes at Camp (first 911 call 06:25 to first burnovers 07:50) and 62 minutes at Carr (aerial warning 18:38 to mayday 19:40). T_detect is the time for the drone to see the hazard: passes every 15 minutes (assumed), each flies with probability p (wind gate) and detects with Pd = 0.9 (assumed). T_notify is the time to get the warning to the crew: a retry every 2 minutes (assumed), each delivered with s = 52%, the TCL 1 telemetry sharing rate with four ground nodes (Wu et al. 2025), used as a stand-in for alert delivery. T_egress is the time the crew needs to reach a safety zone; crew positions are not in the records, so it is shown at 30, 45 and 60 minutes. P(M < 0) is estimated by Monte Carlo: 20,000 random draws of T_detect and T_notify per case, counting how often M comes out negative. How to read the hour strip: one column per hour of the standard day (06:00 to 06:00 local on the peak-run day). Gust mph is the peak wind in that hour at the station named on the document (red when above 30 mph). Alta X 22 and Type 1 at 30 are fly or no-fly: green when that hour's gust is at or under the drone's wind limit, red when above. Map age h is hours since the newest aircraft perimeter in the record. The coloured bars are the drone task we propose for each phase.

## Slide 8
M4 | WATER DROP SUPPRESSION | BOTTOM LINE
Water drops: no drone has done it, so we quantify what the wind allowed
NASA Aerial Wildfire Project | ACERO Disaster Lab | Mission UQ v1.1 | 20 October 2026
8
32 to 53 m
Drift of a 30 m release (assumed) in Camp's standard-day wind, sustained to gust, before aim correction
100%
LNU overnight run hours a 30 kt aircraft (autonomous Firehawk class) could fly by Atlas Peak gusts
35 vs 10,345 L/h
Small drone against large airtanker throughput (Week 6)
Who uses it
Incident commander, operations, air tactical group supervisor: order and sequence drops, especially when crewed aircraft stand down at night.
Crews on the line: they work under the drop.
Drone types and parameters
Autonomous Firehawk: 324 gal bucket (demo), gusts to 30 kt
Seneca Argo-1: 5 drones, 20 gal each (tested)
FireSwarm Thunder Wasp: up to 100 gal (tested)
Large UAS / OPA: night water drop concept (ConOps p.19)
Notes: M4 water drop, bottom line. No drone in the project library has dropped water, so M4 quantifies what the wind would have allowed. First card: drift of 32 to 53 m for a load released from 30 m in Camp's standard-day wind, from the sustained to the gust value, before any aiming correction. Second card: on LNU's overnight run, a 30 kt (34.5 mph) aircraft, the autonomous Firehawk class, could fly 100% of night hours by Atlas Peak gusts. Third card: throughput from the Week 6 workbook, about 35 litres per hour for a small drone against 10,345 for a large airtanker. p, the wind gate, is the share of hours in the standard day when the station wind is at or under the drone's wind limit. Read on sustained wind (10-minute mean) it is the optimistic value; read on gusts (peak in the hour) it is the conservative value. Both are measured 20 ft above ground, so wind at flight altitude is stronger and both overstate availability.

## Slide 9
M4 | WATER DROP SUPPRESSION | HOUR BY HOUR
LNU, 18 to 19 August: the overnight run nobody could see
NASA Aerial Wildfire Project | ACERO Disaster Lab | Mission UQ v1.1 | 20 October 2026
9
Hour
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
23
00
01
02
03
04
05
Gust mph
7
9
8
6
7
10
15
21
28
29
36
36
41
39
29
24
23
22
18
15
11
12
10
15
Alta X 22
Type 1 at 30
Map age h
none
none
none
none
none
none
none
none
none
none
none
none
none
none
none
none
none
none
none
none
none
none
none
none
Drone task
Morning: drones map which drops held and where to drop next
Daylight: helicopter and airtanker drops; drones map where drops held
Night: crewed aircraft stand down; night water drop is a large UAS or OPA concept only
Night: drone IR shows where line held, ready for first light drops
Green: can fly by station gusts. Red: grounded. Dark hour cells: night (20:00 to 06:00). Map age: hours since the newest aircraft perimeter in the record.
What the records show
18:00 Atlas Peak 29 mph sustained, 41 mph gusts
Night Fires merge in a 12-mile overnight run (agency chronology)
00:00 Satellite 41,602 ac for the main object, up from 7,328 ac at 12:00
08:00 First complex ICS-209 (19 Aug): 33,025 ac
Record No aircraft perimeter series exists for LNU without GOFER
Quantified uncertainty
V_eff = n x S x V x P(hit) x p. Wind enters twice: through p and through drift d = u x sqrt(2h/g).
The gust spread of the drift is what an aim on sustained wind cannot remove.
Notes: M4 calculation. Water on target per hour V_eff = n x S x V x P(hit) x p. n is the number of aircraft. S is sorties per hour = 60 / (2 x transit + drop + turnaround), with each term in minutes. V is the load per sortie. p is the wind gate. P(hit) is the chance the drop lands on target: P(hit) = Phi((w - d_res) / sigma) - Phi((-w - d_res) / sigma), where Phi is the standard normal cumulative distribution, w is half the target width, sigma is the aiming error, and d_res is the drift left after the pilot aims for the wind. Drift d = u x sqrt(2h / g): u is wind speed in m/s, h is release height (30 m assumed), g is 9.81 m/s2; sqrt(2h/g) is the fall time, 2.47 s from 30 m. The gust spread, gust drift minus sustained drift, is the part an aim made on sustained wind cannot remove. This is a no-drag, instant-wind estimate; drag and stronger wind aloft pull in opposite directions. How to read the hour strip: one column per hour of the standard day (06:00 to 06:00 local on the peak-run day). Gust mph is the peak wind in that hour at the station named on the document (red when above 30 mph). Alta X 22 and Type 1 at 30 are fly or no-fly: green when that hour's gust is at or under the drone's wind limit, red when above. Map age h is hours since the newest aircraft perimeter in the record. The coloured bars are the drone task we propose for each phase.

## Slide 10
M5 | LOGISTICS SUPPORT | BOTTOM LINE
Logistics: P(on time) for water and supplies to crews
NASA Aerial Wildfire Project | ACERO Disaster Lab | Mission UQ v1.1 | 20 October 2026
10
7.1 to 0.9 km
Alta X loaded radius with 10 kg, still air to Camp's peak 29 mph sustained headwind; zero in its gusts
4% to 71%
Camp standard day P(on time), 3 km delivery inside 30 min (gust to sustained reading)
96% to 100%
Pioneer standard day: remote lines, light wind, so small drones can resupply
Who uses it
Crew bosses and division supervisors: water, hose, pumps and food on remote lines.
Logistics section chief and IC: how many aircraft, which crews by air, which helicopter landing zones stay usable.
Drone types and parameters
Alta X: 22 min at 22 lb, 60 mph top speed, 22 mph limit
Type 3 / 4: radios, batteries, first aid
Elroy Chaparral: 500 lb over 300 nm (in development)
Piasecki KARGO II: 1,500 lb (in development)
Notes: M5 logistics, bottom line. The quantity is P(on time): the chance a requested delivery of water or supplies reaches a crew within its time window. First card: loaded radius of an Alta X carrying 10 kg, 7.1 km in still air and 0.9 km into Camp's peak 29 mph sustained headwind; zero in its gusts, which exceed the assumed cruise speed. Second card: Camp standard day, a 3 km delivery inside 30 minutes is on time in 4% to 71% of hours (gust to sustained reading). Third card: Pioneer's lighter wind gives 96% to 100%. p, the wind gate, is the share of hours in the standard day when the station wind is at or under the drone's wind limit. Read on sustained wind (10-minute mean) it is the optimistic value; read on gusts (peak in the hour) it is the conservative value. Both are measured 20 ft above ground, so wind at flight altitude is stronger and both overstate availability.

## Slide 11
M5 | LOGISTICS SUPPORT | HOUR BY HOUR
Pioneer, 29 August: a flyable day to resupply before the run
NASA Aerial Wildfire Project | ACERO Disaster Lab | Mission UQ v1.1 | 20 October 2026
11
Hour
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
23
00
01
02
03
04
05
Gust mph
6
7
8
8
8
5
5
11
11
13
17
18
18
25
19
9
5
2
3
4
4
5
5
5
Alta X 22
Type 1 at 30
Map age h
13
14
15
16
17
18
19
20
21
22
23
24
1
2
3
4
5
6
7
8
9
10
11
12
Drone task
Resupply crews on remote lines (water, batteries, radios) before the afternoon
Scout helicopter landing zones and drop points ahead of the run
Hold resupply; keep landing zones and safety zones current as the run builds
Night resupply to crews holding line, if authorised
Night: stage loads and check landing zones for first light
Green: can fly by station gusts. Red: grounded. Dark hour cells: night (20:00 to 06:00). Map age: hours since the newest aircraft perimeter in the record.
What the records show
08:00 Newest aircraft perimeter 111,658 ac, already 15 h old
29 Aug About 29,000 ac of growth in the northeastward run
18:16 Aircraft perimeter 140,778 ac; 19:00 ICS-209 111,604 ac, 58% contained
Night 21% of Pioneer perimeters flown at night; about 40% of growth at night
Quantified uncertainty
P(on time) = p x P(complete | fly) x P(cycle <= window). Wind rarely stopped delivery on Pioneer; authorisation and payload do.
Crew demand per shift is not in the records, so fleet size is not computed yet.
Notes: M5 calculation. P(on time) = p x P(complete | fly) x P(cycle <= window). p is the wind gate. P(complete | fly) is the chance a delivery that launches succeeds; set to 1 until a success rate is measured. P(cycle <= window) is the chance the round trip fits inside the delivery window (30 minutes assumed). Loaded radius r = t_usable / (1/(V - w) + 1/(V + w)): t_usable is loaded endurance minus reserve (22 minutes at 22 lb from Week 5, minus 5 minutes reserve), V is cruise airspeed (50 km/h assumed), w is the headwind; flying out against the wind and back with it is what the two terms add up. Cycle = round trip + hold (2 min) + turnaround (10 min), the Week 6 M5 Q4 formula, for a crew 3 km away (assumed). On the slide, P(on time) is the share of standard-day hours that meet both the wind limit and the window. How to read the hour strip: one column per hour of the standard day (06:00 to 06:00 local on the peak-run day). Gust mph is the peak wind in that hour at the station named on the document (red when above 30 mph). Alta X 22 and Type 1 at 30 are fly or no-fly: green when that hour's gust is at or under the drone's wind limit, red when above. Map age h is hours since the newest aircraft perimeter in the record. The coloured bars are the drone task we propose for each phase.